## Slide 1: Adding non-traditional constraints to the embedded systems design process
Indira Jayaram

## Slide 2: Agenda
Goals of the project
Proposed extensions to the embedded systems design process
Design example – camera
Results – comparison of implementations
Other design examples
Conclusions and future work

## Slide 3: Goals of the project
Add nontraditional system requirements to embedded systems design process
Propose extensions to object-oriented design process (UML) through stereotypes
Design example systems using the proposed method
Show how the process leads to making the most reasonable implementation choice

## Slide 4: Basic design process
Object-oriented design process proposed by Bruegge and Dutoit [1]
Steps include :
Requirement elicitation
Development of UML models
Designing the system
Designing the components of the system
Implementing the components
Testing
1. Bernd Bruegge and Alan Dutoit, Object-Oriented Software Engineering Using UML, Patterns, and Java, Third Edition, Prentice Hall, 2010

## Slide 5: Proposed design process
Requirement elicitation, specification
  Functional
  Nonfunctional, traditional—e.g., power usage
  Nonfunctional, nontraditional—e.g., cost
Development of UML models
Designing the system
Designing the components of the system
Implementing the components
Integrating the components
Testing

## Slide 6: Camera example [2]
Requirements | Low-end camera | High-end camera
Resolution | Low (5Million Pixel) | High(12Million Pixel)
Modes | Commonly used Auto modes, no exposure compensation | All parameters changeable – aperture, shutter speed, exposure.
Storage | SD/SDHC memory | CompactFlash
Lens | AF lens | Optical zoom lens
Movie mode | Yes | No
Size | 2.5(w) ,4(h), 1.5(d) inches | 6.2(w), 5.9(h), 3.4(d) inches
Cost | Less than 150 USD | 500-1500 USD
Weight | Less than 8 oz | 30-40oz
Processing speed | Fast enough to be useful (in the range of seconds) | High, owing to many operations
2. Frank Vahid and Tony Givargis, Embedded System Design: A Unified Hardware/Software Introduction, John Wiley & Sons, 2002
.

## Slide 7: Camera example – Use case diagram

## Slide 8: Camera example – Class diagram

## Slide 9: Camera example – Sequence diagram

## Slide 10: Modifying basic design process
UML Lacks support to represent non-functional and non-traditional requirements:
    Solution: Add MARTE annotations [3]
Only way to see if those requirements are satisfied is trial and error:
    Add weighted constraint graphs
3. MARTE home page (Apr 26, 2012), http://www.omgwiki.org/marte

## Slide 11: Proposed extensions to the design proces
Design steps by Bruegge and Dutoit | Proposed extensions | Comments
1.Elicit functional requirements | 1a. List non-traditional requirements | Ex: Size, power,cost,security,reliability, safety, controllability
2. Analyze requirements and generate specifications: Generate: Functional models Object models Dynamic models | 2a. Weight the non-traditional requirements: generate weighted-constraint graphs for the system 2b. Generate weighted-constraint graphs for different classes in the object model 2c. Annotate the object models to reflect non-traditional properties by applying MARTE’s NFP and GRM profiles 2d. Annotate the dynamic models to reflect time-based operations by applying MARTE’s Time profile 2e. Annotate the dynamic models to indicate the classes responsible for fulfilling the timing requirements | System acceptance tests should be defined during this step also.

## Slide 12
Basic process | Extensions | Comments
3. Design the system : Map subsystems into components Design global control flow Identify boundary conditions Decide on the trade-offs from functionality perspective | 3’. Decide on the trade-offs with the non-traditional properties taken into consideration | System level tests should be defined during this step
4. Design the objects in the system: Reuse existing off-the shelf components Specify interfaces - Optimize |  | The non-traditional constraints will be considered during design and they have been integrated into the requirement and specification steps
5. Map the object model to the interface platform |  | Implementation level tests should be defined during this step
6. Test: Plan the tests by considering the tests that have been defined Test the units Test the integrated units Test for usability | 6a. Test the system for performance on non-traditional properties front 6b. Verify if the performance matched the requirements as specified in the weighted constraint charts | 
.

## Slide 13
MARTE (Modeling and Analysis of Real Time and Embedded Systems) – set of UML profiles to represent NFPs [4]
4. MARTE Tutorial, http://www.omg.org/omgmarte/Tutorial.htm

## Slide 14
MARTE Time profile

## Slide 15: Weighted constraint charts
Constraints (requirements) are weighted in the order of how crucial they are.
Weights add up to 100
Requirements-> | Req1 | Req2 | Req3 | Req4 | Req5
Weights-> | W1 | W2 | W3 | W4 | W5
Chart: 
| Req1 | Req2 | Req3 | Req4 | Req5
 | 10 | 20 | 30 | 10 | 30

## Slide 16: Caveats
Weights are decided intuitively. Currently, no theoretical basis to decide.
Main purpose of using weights is to consider the relative importance of constraints rather than giving them absolute values.
For example, could equate weights to “critical”, “important”, “desirable”, “nice to have”.
Weights can be refined in an organization as the organization’s process becomes more mature.

## Slide 17: Modified camera example: applying extended design steps

## Slide 18
Sequence diagram with time values
Modified camera example: applying extended design steps

## Slide 19: Weighted constraint charts for high-end and low-end cameras

## Slide 20
Components that make up the system must be chosen in such a way that they satisfy the constraints
To see how the constraints can be met by different combinations of the components, weighted constraint charts are to be drawn for the classes (which lead to components) of the system

## Slide 21: Weighted constraint charts for components of low-end camera

## Slide 22: Weighted constraint charts for components of high-end camera

## Slide 23: Implementation of a simple camera control system
Very low-end version. Img resolution = 64*64 pix, Processing time < 10s
Implementation platform – Altera UP3 FPGA board with NIOS soft core processor
Make use of off the shelf components with known specifications

## Slide 24: Basic Flow diagram and constraint chart

## Slide 25: Constraint charts for components

## Slide 26: Comparison of available off-the shelf components and previous implementations
Software implementation on 8051 platform [2]
Performance: 9s at 12MHz, Complexity: 98k gates
JPEG encoder hardware[5]:
Performance: 1s at 25MHz, Complexity: 10k logic
elements on Altera UP3 board
CCD processor hardware[4]:
Performance: 0.2s at 25MHz, Complexity: 8k
gates in Verilog
5. James Rosenthal, JPEG image compression using an FPGA, M.S. Thesis, EE Dept. UC Santa Barbara, 2006

## Slide 27: A few possible implementations
Software implementation : Port the code available for 8051 platform to suit the NIOS core
Hardware implementation: Use the JPEG encoder hardware, CCD processor hardware and come up with hardware logic for general controls
Mixed implementation 1: Use the JPEG encoder hardware along with the software components for all other blocks
Mixed implementation 2: Use the CCD processor hardware along with software components for remaining blocks

## Slide 28
Based on the constraint charts drawn previously, implementation 3 seems like the best choice:
  1st implementation barely meets time constraint
  2nd implementation barely meets cost constraint—uses 98% of chip area; if any changes are needed, a larger chip must be chosen; also ease of upgrade is very low
  3 and 4 are comparable; values for 3 are closest to values in the constraint graph

## Slide 29: Results of implementation on UP3 board

## Slide 30: Implementation 2

## Slide 31: Implementation 3

## Slide 32: Implementation 4

## Slide 33: Comparison of implementations
 | Processing time | Logic elements | Memory usage | Pin usage
Implementation 1 | 8s | 11% | 18% | 1%
Implementation 2 | 1s | 98% | 20% | 32%
Implementation 3 | 6s | 18% | 18% | 2%
Implementation 4 | 3s | 87% | 17% | 14%

## Slide 34
Implementations 3 and 4 are the main contenders. A closer comparison:
Implementation 3 is better.
 | Speed | Cost | Ease of use | Upgrades
Implementation 3 | x | y | High | Very easy
Implementation 4 | 2x | 4y | Very high | Easy

## Slide 35: Other systems designed [6]
GPS
6. Indira Jayaram, Adding non-traditional constraints to the embedded systems design process, MS thesis, Univ. of Cincinnati, 2011.

## Slide 36: GPS

## Slide 37: GPS
Annotated sequence diagram

## Slide 38: Weighted constraint charts for GPS
Chart: 
| Small size | Low Cost | Low Power | Real-time responsiveness | Low Weight | Safety | Reliability | Resistance to environmental conditions | Security | Controllability | Upgrades | High Speed
Low-end GPS | 30 | 35 | 10 | 10 | 5 | 0 | 5 | 0 | 0 | 0 | 0 | 5
High-end GPS | 5 | 5 | 5 | 20 | 5 | 5 | 5 | 10 | 30 | 0 | 0 | 10

## Slide 39: Weighted constraint charts for components of GPS

## Slide 40: ABS

## Slide 41: ABS

## Slide 42: ABS
Annotated sequence diagram

## Slide 43: Weighted constraint chart for ABS
Chart: 
| Small size | Low Cost | Low Power | Real-time responsiveness | Low Weight | Safety | Reliability | Resistance to environmental conditions | Security | Controllability | Upgrades | High Speed
High-end GPS
ABS | 2 | 0 | 0 | 25 | 0 | 25 | 20 | 20 | 5 | 2 | 0 | 1

## Slide 44: Weighted constraint chart for components of ABS

## Slide 45: Conclusions
Annotating class diagrams and sequence diagrams with NFPs and NTPs helps in understanding the dependencies
Weighting the constraints aids in making better design and implementation choices

## Slide 46: Future work
Standard weighting scales have to evolve
Need a better way of representing qualitative NTPs.
Tools?