## Slide 1
Performance Analysis and Optimization
(General guidelines; Some of this is review)
Outline:
introduction
evaluation methods
timing
space—code compression
power

## Slide 2
Performance: how can we optimize performance?
Time
Space
Power
(cost)
(weight)
{development time, ease of maintenance, extensibility}

## Slide 3: Methods for analyzing performance
Instruction counting
Simulation
Measurement of actual system in action

## Slide 4: Some guidelines (evaluation):
1. Don’t spend a lot of time optimizing a feature which contributes little to overall system performance
Don’t use hardware-independent metrics
ex: code size: inline functions will increase code size but can make the code faster because you are avoiding function calls
Remember that “peak performance” is only a boundary value; it may not be achievable under normal conditions
Don’t use just one metric, e.g., higher clock rate—this may not tell the whole story
Don’t use “synthetic” benchmarks, use REAL benchmarks from the problem domain you are in
ex: “random” graphs are not “circuit” graphs

## Slide 5: Timing

## Slide 6
Arithmetic—basic algorithms
Hierarchy of time complexity:
increment / decrement
addition / subtraction
multiplication increasing execution time
division / square root
other operations
can often trade off time for space
Example: addition of 2 16-bit numbers
carry-ripple adder:
time - 31 gate delays
space - 16 full adders
carry lookahead adder (4-bit units):
time – 8 gate delays
space – 4 4-bit CLA units—more gates, routing

## Slide 7: fig_14_00
fig_14_00
Example: summing array elements—linear in size of array

## Slide 8: table_14_00
table_14_00
How to analyze performance and
Do optimizations

## Slide 9: fig_14_02
fig_14_02
Time complexity: loops--examples
Execution time proportional to N
Execution time proportional to 100—easier to analyze time but not so flexible

## Slide 10
Common data structures (not dynamic):
Array:
O(n) [move]:
Insert / delete at beginning
Insert / delete at end
Insert / delete in middle
O(1):
Access at beginning
Access at middle
Access at end

## Slide 11
Common data structures (not dynamic):
Linked list:
O(1):
Insert / delete at beginning
access at beginning
O(n):
insert / delete at end (or O(1) if extra pointer)
insert / delete in middle
Access at middle
Access at end (or O(1) if extra pointer)

## Slide 12: fig_14_09
Flow of control:
1—what is addressing mode? How long does it take to access a variable?
Common modes, relative times:
Immediate < register < direct < indirect < double indirect …
Must also consider cache and virtual memory overheads
2—standard control flows: how much time is required?
sequential
loops / conditionals
function calls: context switch
(e.g., is overhead of recursion justified?)
co-routines: e.g., 2 subfunctions operating in turn,
controlled by a “manager” function
interrupts: similar to function call, no variables passed

## Slide 13: fig_14_21
fig_14_21
Example: function call--what happens at machine level:

## Slide 14: fig_14_26
fig_14_26
Response time—2 systems

## Slide 15: fig_14_27
fig_14_27
Best and worst case times

## Slide 16: fig_14_29
fig_14_29
Memory: hierarchy / response times

## Slide 17: Some guidelines (implementation):
Use lookup tables or combinational logic (for multiplication, e.g.)
Considering using shifts for mathematical calculations
Study compiler optimization techniques
Optimize loops
example: loop unrolling
example:
for (j=0; j<x+3;j++)  endVar = x+3; for (j=0; j< endVar; j++)
example: can you replace nested loops by one loop on a multidimensional array?
5. use case instead of multiple if-else statements

## Slide 18: Some guidelines (implementation-continued):
Use registers and caching
Optimize the most frequently used code paths and code blocks
Know when to choose recursion versus iteration
Use macros and inline functions where appropriate

## Slide 19: Implementation of bitmask based code compression algorithm on MSP430 microcontroller (excerpts)
Lijo John
Spcae--Code compression

## Slide 20: Motivation
Embedded systems:
Real-time performance at a low cost
Compact in size
Minimal power consumption
Embedded systems memory:
  Major design constraint
  Impacts
    Cost
    Size
    Power Consumption
    Chip area

## Slide 21: Code compression
Application Program
(Binary)
Compression
Algorithm
Processor
(Fetch and Execute)
Decompression
Engine
Compressed Code
(Memory)
Static Encoding
(Offline)
Dynamic Decoding
(Online)

## Slide 22: Decompression Engine (DCE)
Two options:
  Pre-cache design
    Between memory and cache
  Post-cache design
    Between cache and processor
    Cache holds compressed data
    Reduced bus bandwidth and higher cache hits
Main
Memory
Pre-Cache
DCE
D-Cache
D-Cache
Processor
Post-Cache
DCE
Bus
Bus

## Slide 23: Compression Ratio
Compression ratio
Smaller compression ratio is better

## Slide 24: Summary of code compression algorithms
Reference numbers—see thesis

## Slide 25: Compression Techniques
Dictionary based approach
  Good compression ratio
  Fast decompression scheme
Hamming distance based approach
  Limited: profitable only up to 3 bit mismatches
Bitmask based approach
  Uses bitmasks to maximize matching patterns
  Improves compression ratio even further than dictionary based approach

## Slide 26: Traditional dictionary-based code compression
Format for Uncompressed Code (32 Bit Code) Format for Compressed Code
Uncompressed Data
(32 Bits)
Decision
(1 Bit)
Dictionary Index
Decision
(1 Bit)
0000 0000
1000 0010
0000 0010
0100 0010
0100 1110
0101 0010
0000 1100
0100 0010
1100 0000
0000 0000
0 0
1 1000 0010
1 0000 0010
0 1
1 0100 1110
1 0101 0010
1 0000 1100
0 1
1 1100 0000
0 0
0 – Compressed
1 – Not Compressed
Index | Entry
0 | 0000 0000
1 | 0100 0010
Original Program
Compressed Program
Dictionary
Original code size = 80 bits
Compressed code size = 62 bits
Dictionary size = 16 bits
Compression ratio = (62+16)/80
= 97.5%

## Slide 27: Mismatch based code compression (also dictionary)
Format for Uncompressed Code Format for Compressed Code
Uncompressed Data
(32 Bits)
Decision
(1 Bit)
Decision
(1 Bit)
# of Bit
Changes
Dictionary
Index
Location
(5 Bits)
Location
(5 Bits)
… …
0000 0000
1000 0010
0000 0010
0100 0010
0100 1110
0101 0010
0000 1100
0100 0010
1100 0000
0000 0000
0 1 0
1 1000 0010
0 0 110 0
0 1 1
1 0100 1110
0 0 001 0
1 0000 1100
0 1 1
1 1100 0000
0 1 0
0 – Compressed
1 – Not Compressed
0 – Mismatch
1 – No Action
Index | Entry
0 | 0000 0000
1 | 0100 0010
Mismatch Position
Original Program
Compressed Program
Dictionary
Original code size = 80 bits
Compressed code size = 60 bits
Dictionary size = 16 bits
Compression ratio = 95%

## Slide 28: Bitmask Technique
Generate repeating patterns aggressively
Traditional dictionary and mismatch based techniques are inefficient!
XOR operation: simple and fast
0000 0000 0010 1101
1111 0100 0010 0001
11
0001
111101
In Dictionary
0000 0000 0010 0001
0000 0000 0011 0001

## Slide 29: Bitmask encoding
32-bit instructions
Format for uncompressed code
Format for compressed code
Uncompressed Data
(32 Bits)
Decision
(1 Bit)
Decision
(1 Bit)
Mask
(1 Bit)
…
Mask
Type
Location
Mask
Pattern
Mask
Type
Location
Mask
Pattern
Dictionary
Index

## Slide 30: Bitmask based code compression
0000 0000
1000 0010
0000 0010
0100 0010
0100 1110
0101 0010
0000 1100
0100 0010
1100 0000
0000 0000
0 1 0
0 0 00 11 1
0 0 11 10 0
0 1 1
0 0 10 11 1
0 0 01 01 1
0 0 10 11 0
0 1 1
0 0 00 11 0
0 1 0
0 – Compressed
1 – Not Compressed
0 – Bit Mask Used
1 – No Bit Mask Used
Index | Entry
0 | 0000 0000
1 | 0100 0010
Dictionary
Compressed Program
Bit Mask Position
Bit Mask Value
Original Program
Original code size = 80 bits
Compressed code size = 54 bits
Dictionary size = 16 bits
Compression ratio = (54+16)/80
= 87.5%

## Slide 31: Compression algorithm
Algorithm: Bitmask based code compression
Input: Original code (binary) divided into 16-bit vectors
Output: Compressed code and dictionary
Begin
Step1: Create the frequency distribution of the 16-bit vectors
Step 2: Create the dictionary based on Step 1
Step 3: Compress each 16-bit vector using bitmask
Step 4: Handle and adjust branch targets
return Compressed code and dictionary
End

## Slide 32: Branch targets
Approach for handling branch targets
  Map the branch target addresses in the original code onto new target addresses in the compressed code
  Fast retrieval of the new target address

## Slide 33: Decompression core

## Slide 34: Evaluation: Target Architecture
Texas Instrument’s 16-bit MSP430 microcontroller
  Designed for a wide range of low power and portable applications
  Applications include metering devices, portable medical devices, data logging and wireless communications, capacitive touch-sense IOs, energy harvesting, motor control and security and safety devices
  Compression not implemented for this processor previously

## Slide 35: Code Outline

## Slide 36: Experimental setup
Code developed in C++ and compiled using gcc compiler
Collected sample code programs for MSP430 microcontroller from TI website (website address)
Compiled programs using TI Code Composer Studio v4.0
Implemented the bitmask based code compression algorithm on the binary files generated after compilation

## Slide 37: Experimental setup cont.
In our experiments, we implemented three test cases
  Test case 1: Applied a 2-bit mask
  Test case 2: Applied a 4-bit mask
  Test case 3: Applied a 8-bit mask
We computed the compression ratio for all three test cases
20 programs, 5 omitted because they were very similar to other programs

## Slide 38: Sample code programs

## Slide 39: Experimental results
Achieved a compression ratio of 62 -76%
(from [1])
Min
Max

## Slide 40: Experimental results cont.
Compression ratio for ADC10_ex1
  For code size below 10000 bytes
Chart: Mask size (bits)
| 2 | 4 | 8
2-bit mask | 63.54
4-bit mask | 62.1
8-bit mask | 64.22

## Slide 41: Experimental results cont.
Compression ratio for crc_ex1_DCOSetup
  For code size above 10000 bytes
Chart: Mask size (bits)
| 2 | 4 | 8
2-bit mask | 66.85
4-bit mask | 71.58
8-bit mask | 68.42

## Slide 42: Result summary

## Slide 43: Result summary cont.

## Slide 44: table_14_03
table_14_03
Power:
Power usage for some common operations:

## Slide 45: fig_14_30
fig_14_30
Power—sophisticated management possible

## Slide 46: fig_14_31
fig_14_31
Using a power manager

## Slide 47: fig_14_32
fig_14_32
Power management schemes

## Slide 48: fig_14_33
fig_14_33
Standard power modes